Interface $managementinterfacename
ip address $mangementinterfaceip $subnetmask
exit
#if($destinationprefix != "" && $destinationmask != "" && $forwardingaddress != "")
ip route $destinationprefix $destinationmask $forwardingaddress
#end

#if (${InterfaceName})
        interface ${InterfaceName}
       #if (${Description} != "")
        description ${Description}
        #end
        #if(${A1} == "Access")
        switchport mode access
        #if(${StaticAccessVLan} != "")
        switchport ACCess vlan ${StaticAccessVLan}
        #end
        #end

       #if(${A1} == "Trunk")
        switchport mode trunk
        #if(${TrunkAllowedVLan} != "")
        switchport trunk allowed vlan ${TrunkAllowedVLan}
        #end
        #if(${NativeVLan} != "")
        switchport trunk native vlan ${NativeVLan}
        #end
        #end

        #if(${A1} == "Dynamic Auto")
        switchport mode dynamic auto
        #end

        #if(${A1} == "Dynamic Desirable")
        switchport mode dynamic desirable
        #end

        #if(${VoiceVlan} != "")
        switchport voice vlan ${VoiceVlan}
        #end

        #if(${PortFast} != "")
        #if(${PortFast} == "Disable")
        no spanning-tree portfast
        #elseif(${PortFast} == "Enable")
        spanning-tree portfast
        #end
        #end

        #if(${spd}!= "")
        #if(${spd} == "Auto")
        speed auto
        #elseif(${spd} == "10 Mbps")
        speed 10
        #elseif(${spd} == "100 Mbps")
        speed 100
        #elseif(${spd} == "1000 Mbps")
        speed 1000
        #end
        #end

        #if(${duplexField}!= "")
        #if(${duplexField} == "Auto")
        duplex auto
        #elseif(${duplexField} == "Half")
        duplex half
        #elseif(${duplexField} == "Full")
        duplex full
        #end
        #end
exit
#end

#if($option == "dhcp")
        ip address $dhcp
        #elseif($option == "static")
        ip address $address $subnet
        #end
#end

#foreach ($InterfaceName in $gv.InterfaceNameList)
    interface $InterfaceName
        shutdown
    exit
#end

5254.0013.C7A2
5254.0001.A045

description <==MAB==>
 switchport access vlan 100
 switchport mode access
 switchport nonegotiate
 authentication host-mode multi-domain
 authentication port-control auto
 authentication periodic
 authentication timer restart 3600
 authentication timer reauthenticate 600
 authentication violation restrict
 mab
authentication open
 spanning-tree portfast

*Apr 8 16:40:44.914: ARP Packet (Gi0/0/10) SM: 5254.0002.4cbc, SI: 192.168.10.1, TM: 5254.0013.c7a2, TI: 192.168.10.9

*Apr 8 16:40:44.935: ARP Packet (Gi0/0/10) Src: 5254.0013.c7a2, Dst: 5254.0002.4cbc, SM: 5254.0013.c7a2, SI: 192.168.10.9, TM: 5254.0002.4cbc, TI: 192.168.10.1

*Apr 8 16:40:44.936: No L3 idb for vlan 10 to send to CPU

*Apr 8 16:40:44.937: Dst mac of the arp packet matches switch's mac.

*Apr 8 16:40:51.821: ARP Packet (Gi0/1/10) SM: 5254.0014.beb2, SI: 192.168.10.1, TM: 5254.0001.a045, TI: 192.168.10.7

*Apr 8 16:40:51.840: ARP Packet (Gi0/1/10) Src: 5254.0001.a045, Dst: 5254.0014.beb2, SM: 5254.0001.a045, SI: 192.168.10.7, TM: 5254.0014.beb2, TI: 192.168.10.1

*Apr 8 16:40:51.841: No L3 idb for vlan 10 to send to CPU

*Apr 8 16:40:51.842: Dst mac of the arp packet matches switch's mac.

*Apr 8 16:41:21.952: ARP Packet (Gi0/0/10) SM: 5254.0002.4cbc, SI: 192.168.10.1, TM: 5254.0013.c7a2, TI: 192.168.10.9

*Apr 8 16:41:30.145: ARP Packet (Gi0/1/10) SM: 5254.0014.beb2, SI: 192.168.10.1, TM: 5254.0001.a045, TI: 192.168.10.7

.
bcffc2

conf t
username cisco password cisco
enable password cisco
ip domain name cisco.com
no ip domain lookup
crypto key generate rsa mod 2048
!
ip ssh version 2
!
line vty 0 15
login local
transport input ssh
transport preferred ssh
transport output ssh

   TNOW = end_time - start_time
    print('#' * 50)
    print(f'It took {TNOW} for the script to run.')
    print('#' * 50)

class Testclass:
    age = 0
    sex = " "
    def __init__(self, age, sex):
        self.age = age
        self.sex = sex

    def fox(self):
        print("Your age is " + self.age + "\nYou are a " + self.sex)

import paramiko
from netmiko import ConnectHandler
from getpass import getpass
import time
from datetime import datetime

class RouterScript:

    def __init__(self, IP, username, password):
        self.IP = IP
        self.username = username
        self-password = password

    def connect(self):
        with open ('router_list') as list:
        for IP in list:
        VIRL_DEVICES = {
        'device_type': 'cisco_ios',
        'host': self.IP,
        'username': 'self.username',
        'password': 'self.password',
        'global_delay_factor': 4
        }

        print ('Connecting to the device ' + IP)
        net_connect = ConnectHandler(**VIRL_DEVICES)
        time.sleep(2)

        with open ('config', 'r') as CONFIG_LINES:
        CONFIG = CONFIG_LINES.readlines()
        time.sleep(1)
        output = net_connect.send_config_set(CONFIG)
        print(output)
        time.sleep(3)

    def start_time(self):
        start_time = datetime.now().replace(microsecond=0)
        return start_time
    def end_time(self):
        end_time = datetime.now().replace(microsecond=0)
        return end_time

RADIUS Filter-ID Attribute Direction
Remote Authentication Dial In User Service (RADIUS) filter-ID attribute direction enhancement introduces
support for manipulating the direction in which the RADIUS attribute filter-ID is applied. RADIUS attribute
filter-ID specifies the access list (ACL) that is applied to the subscriber interface.
When the RADIUS filter-ID attribute defined in RFC-4849 is applied to a subscriber session, it is by default
applied in the output direction of the corresponding subscriber interface. The RADIUS filter-ID attribute
direction can be changed using the command radius-server attribute 11 default direction inbound in global configuration.
Restrictions
The RADIUS filter-ID attribute direction enhancement has these restrictions:
• The radius-server attribute 11defaultdirectioninboundcommand is global, that is, change is applied
to all new subscriber sessions established after the configuration change. Existing sessions are not
modified.
• This enhancement is only to change direction in RADIUS. It is not possible to change direction in Cisco
IOS XR CLI if ACL is sent by RADIUS.

Configuring RADIUS Filter-ID Attribute Direction: Example
The following example shows how to configure RADIUS filter-ID attribute direction:

configure
radius-server attribute 11 default direction inbound

aaa authentication dot1x default group WINSERVER
aaa authorization network default group WINSERVER
aaa authorization auth-proxy default group WINSERVER
aaa authorization console
aaa accounting dot1x default start-stop group WINSERVER
!
!
aaa server radius dynamic-author
 client 192.168.100.20 server-key Nikita1980!
!
!
radius server RAD2
 address ipv4 192.168.100.20 auth-port 1812 acct-port 1813
 timeout 10
 key Nikita1980!
!
radius-server attribute 6 on-for-login-auth
radius-server attribute 6 support-multiple
radius-server attribute 8 include-in-access-req
radius-server attribute 25 access-request include
radius-server attribute 31 mac format ietf upper-case
radius-server attribute 31 send nas-port-detail
radius-server dead-criteria tries 2
radius-server deadtime 30
!
aaa group server radius WINSERVER
 server name RAD2
!
!
!
aaa new-model
aaa session-id common
!
!